## Slide 1
The SPEX instrument
measurement concept, polarimetric calibration,
ground-based measurements
Gerard van Harten, Leiden Observatory, The Netherlands
Polarimetric Techniques & Technology, March 24, 2014, Leiden
Frans Snik
Christoph Keller
Jeroen Rietjens
Martijn Smit
Antonio di Noia
Otto Hasekamp
Hester Volten

## Slide 2
Atmospheric aerosols
Size
Shape
Chemical composition

## Slide 3
Measurements
Intensity + polarization
Multiple wavelengths
Multiple scattering angles

## Slide 4
Measurements
Hasekamp+ (2011)

## Slide 5
400-800 nm
30 viewing angles
ΔP=0.001+0.005.P
Snapshot
Low power
Small size
Low complexity
Modularity
Instrument requirements
Mishchenko+ (2004)
Hasekamp+ (2007)

## Slide 6
Polarization modulation
Temporal modulation: rotating polarizer or waveplate, or liquid crystal.
Timing issues; Risk of failure; large power consumption.
2. Spatial modulation: split up beam according to four (three) linear polarization directions.
Differential transmission; Large.
Spectral modulation: a sinusoidal modulation on the measured intensity spectrum.
Degree of Linear Polarization (DoLP)  Amplitude
Angle of Linear Polarization (AoLP)  Phase

## Slide 7
SPEX polarimetry
DoLP variation
AoLP variation
courtesy: Jeroen Rietjens (SRON)

## Slide 8
SPEX polarimetry
Snik+ (2009)

## Slide 9
Polarimetric trade-off
Advantages of spectral modulation:
Fully passive
Scalable
One-shot measurement
No differential effects
Disadvantages:
Spectrograph
Spectral oversampling

## Slide 10
Dual-beam spectral modulation
Intensity at full resolution
No aliasing  accurate radiometry & DoLP
Redundancy  differential transmission correction
Beam-exchange polarimetry  averages out dark & differential transmission
Snik+ (2009)
Craven+ (2009)
Van Harten+ (2014a)

## Slide 11
190 mm
100 mm
60 mm
SPEX prototype
spectral range: 400-750 nm
spectral resolution (flux): 2.5 nm
spectral resolution (polarization): 20 nm
volume: 2 dm3
mass: 2 kg

## Slide 12
SPEX prototype
100 mm
60 mm
spectral range: 400-750 nm
spectral resolution (flux): 2.5 nm
spectral resolution (polarization): 20 nm
volume: 2 dm3
mass: 2 kg
190 mm
No instrumental
polarization

## Slide 13
SPEX prototype
100 mm
60 mm
spectral range: 400-750 nm
spectral resolution (flux): 2.5 nm
spectral resolution (polarization): 20 nm
volume: 2 dm3
mass: 2 kg
190 mm
Fresnel
rhomb
MgF2
Al2O3
Athermal

## Slide 14
SPEX prototype
Simulation
Measurement
courtesy: Jeroen Rietjens (SRON)

## Slide 15
Polarization calibration
DoLP

## Slide 16
Polarization calibration
AoLP

## Slide 17
Polarization calibration
DoLP accuracy
courtesy: Jeroen Rietjens (SRON)

## Slide 18
Polarization calibration
DoLP error
courtesy: Jeroen Rietjens (SRON)

## Slide 19
Polarization calibration
DoLP sensitivity
courtesy: Jeroen Rietjens (SRON)

## Slide 20
Polarization calibration
DoLP error
courtesy: Jeroen Rietjens (SRON)

## Slide 21
Sky measurements
Ground-based SPEX instrument
Space prototype
Meteorological site w/ AERONET
Off-the-shelf components
Low-cost
courtesy: Jos de Boer

## Slide 22
Sky measurements
Raw spectral data
Van Harten+ (2014b)

## Slide 23
Sky measurements
.....
Measurement & retrieval
courtesy: Antonio di Noia (SRON)

## Slide 24
Sky measurements
Aerosol parameters
courtesy: Antonio di Noia (SRON)

## Slide 25
Sky measurements
courtesy: Antonio di Noia (SRON)

## Slide 26
Spectral line polarimetry
Spectrograph
Aerosol vertical profiling
Line polarization?
Differential transmission correction
Van Harten+ (2014a)

## Slide 27
Spectral line polarimetry
Spectrograph
Aerosol vertical profiling
Line polarization?
Differential transmission correction
Van Harten+ (2014a)

## Slide 28
Spectral line polarimetry
O2A band + continuum polarization
Van Harten+ (2014a)

## Slide 29
Outlook
Operational ground-based instrument
Flight campaign prototype

## Slide 30
SPEX
Demonstration prototype
during lunch break!
Polarimetric Techniques & Technology, March 24, 2014, Leiden
Frans Snik
Christoph Keller
Jeroen Rietjens
Martijn Smit
Antonio di Noia
Otto Hasekamp
Hester Volten